Small Unmanned Aircraft Systems

sUAS

Small Unmanned Aircraft Systems

sUAS

STANDARD OPERATING GUIDELINES

Revision 2

Contents

Introduction	1

sUAS Federal Rule/Policy 14 CFR Part 107	1

Flight Crew	2

Remote Pilot in Command (remote PIC)	2

Flight Operator (FO)	3

Visual Observer (VO)	4

Site Manager (SM)	5

Operating Requirements	5

Planning for flight Missions	6

Small Unmanned Aircraft System (sUAS)	8

General‐Purpose UAS Checklist	11

Small Unmanned Aircraft System FLIGHT LOG	12

Introduction

The small Unmanned Aircraft System Standard Operating Guidelines (sUAS SOG) is intended to guide the use and operation of small unmanned aircraft systems (sUAS) to serve the functions of the Tennessee Department of Transportation. Such operations shall be conducted under the Code of Federal Regulations 14 CFR Part 107 issued by the Federal Aviation Agency.

Modifications were made to reflect additional requirements by TDOT to enhance the safety and efficiency of the sUAS flight operations.

These guidelines do not address every possible scenario and contingency that can arise nor is it inclusive of all rules of safety and adequate standard practice. However, these SOG provide a process that ensures regulated consistent operations. Operators of the sUAS are directly responsible for their conduct and are expected to account for variations that may arise from all the factors affecting the sUAS flight operation.

All personnel operating under these guidelines shall be in compliance with all applicable Federal Aviation Regulations (FARs) and state and local laws. The FAA regulations shall take precedence over these guidelines if any discrepancy may arise.

Waivers of operational restrictions may be requested from the FAA. Application for such waiver must demonstrate the proposed operation can be conducted safely with the requested waivered requirements. Such waivers shall be obtained by TDOT prior to the application of any waived rules or limitations to flight operations.

sUAS Federal Rule/Policy 14 CFR Part 107

In 2012, Congress passed the FAA Modernization and Reform Act of 2012 (PL 112‐95). PL 112‐ 95, Section 333 directed the Secretary of Transportation to determine whether UAS operations posing the least amount of public risk, and no threat to national security, could safely be operated in the NAS. Section 333, established requirements for the safe operation of these systems in the NAS, prior to completion of the UAS comprehensive plan and rule makings required by PL 112‐95, Section 332. On February 23, 2015, as part of its ongoing efforts to integrate UAS operations in the NAS and in accordance with PL 112‐95, Section 333, the FAA issued a Notice of Proposed Rule Making (NPRM) proposing to amend its regulations to adopt specific rules for the operation of sUAS in the NAS. In consideration of the public comments to the proposed rule, the FAA issued a final rule adding part 107, integrating civil sUAS into the NAS. Part 107 allows sUAS operations for many different non‐hobby and non-recreational purposes without requiring airworthiness certification, exemption, or a Certificate of Authorization (COA).

By issuing Part 107 (effective August 29th, 2016), the FAA addressed aviation safety in three key areas: personnel, equipment, and operations. The FAA assessed each of these areas both independently to meet current regulations and standards, as well as collectively to ensure no conflicts exist overall that would create an unsafe condition. This approach allows the FAA to be flexible in responding to the needs of the aviation community while still being able to establish standards for future growth and development. To that end, part 107 contains subparts that focus on each of these key aviation safety areas specific to sUAS.

More specific details pertaining to 14 CFR Part 107 are available through the FAA website: https://www.faa.gov/uas/resources/uas_regulations_policy/

Flight Crew

The Flight Crew may include remote PIC, Visual Observers, Operators, and any other personnel necessary for the safe conduct of flight operations. All Flight Personnel should be fully qualified to perform their duties safely and effectively.

All Flight Personnel must be in a condition fit to perform their duties safely. No person may act as a member of the Flight Personnel if they are under the influence of any drug, alcohol, or medication likely to impair their performance of duties.

Remote Pilot in Command (remote PIC)

The operation of the sUAS shall be under the command of the Remote Pilot‐in‐Command (remote PIC) who has all the responsibility and authority of the remote PIC as described by 14 CFR Part 107 and AC 107‐2. The remote PIC has ultimate responsibility for the safe operation of the UAS. As a result, the remote PIC has the final decision on whether to initiate or terminate any flight.

Remote PIC Duties and Responsibilities

·	The remote PIC shall have a remote pilot certificate with a sUAS Rating accessible during flight operations or its equivalent.

·	The remote PIC will have the final authority and responsibility for the operation and safety of the sUAS operation.

·	The remote PIC shall evaluate and approve each mission and is responsible to recognize risk and refuse all missions with unacceptable risk.

·	Before launch, the remote PIC must understand the mission request and have all applicable documentation at the ground control station.

·

·	The remote PIC is required to be aware of weather forecasts, winds, hazards, temporary flight restrictions, and all pertinent information necessary to perform the mission.

·	The remote PIC will send completed flight logs to the Division of Aeronautics UAS Program Monitor.

·	The Remote PIC will notify their supervisor, and the UAS section in the Aeronautics Division, immediately if their license should no longer be valid.

Qualifications

·	The remote PIC must hold a valid U.S. driver’s license valid within the state of Tennessee.

·	The remote PIC must hold a valid remote pilot certificate with a sUAS rating or its equivalent.

·	The PIC shall maintain an appropriate level of understanding of the FARs applicable to the airspace including 14 CFR Part 107 where UAS operations will occur.

·	No one may act as remote PIC unless they have read and familiarized themselves with the contents of these guidelines and the specific Operator’s Manual for the sUAS they will fly.

·	All remote PIC candidates must be approved by the TDOT Aeronautics Division, before serving as remote PIC for TDOT sUAS flight operations.

Training and Currency

·	The remote PIC must be trained on the ability to safely operate the sUAS in a manner consistent with how the sUAS will be operated including evasive and emergency maneuvers and maintaining appropriate distances from persons, vessels, vehicles, and structures.

·	In order to be current, the remote PIC must have conducted and logged at least 3 launch and 3 recovery operations within the previous 90 days. These operations must have been conducted on a registered sUAS of the same class as the sUAS to be used, and in a comparable environment.

·	Training flights must be conducted to maintain proficiency.  Only the remote PIC can determine their individual training requirements.  Training requirements should be based on the remote PIC’s level of experience, the type of mission, operating environment, and familiarity with the particular UAS.  The remote PIC should train often enough to ensure that the highest level of safety will be maintained.

Flight Operator (FO)

The Flight Operator (FO) may operate the sUAS under the command of the Remote Pilot‐in‐ Command (remote PIC) who has all the responsibility and authority of the remote PIC as described by 14 CFR Part 107 and AC 107‐2. The FO is responsible for his or her actions and the safe operation of the UAS under the direction of the remote PIC. The remote PIC has the final decision on whether to initiate or terminate any flight.

Duties and Responsibilities

·	The FO shall operate the sUAS under the direct command of the remote PIC

·	Before launch, the FO must understand the mission request and have all applicable documentation at the ground control station.

·	The FO is required to be aware of weather forecasts, winds, hazards, temporary flight restrictions, and all pertinent information necessary to perform the mission.

Qualifications

·	The FO must hold a valid U.S. driver’s license valid within the state of Tennessee.

·	The FO shall maintain an appropriate level of understanding of the FARs applicable to the airspace including 14 CFR Part 107 where UAS operations will occur.

·	No one may act as FO unless they have read and familiarized themselves with the contents of these guidelines and the specific Operator’s Manual for the sUAS they will fly.

·	All FO candidates must be approved by the remote PIC before serving as FO for TDOT sUAS flight operations.

Training and Currency

·	The FO must be trained on the ability to safely operate the sUAS in a manner consistent with how the sUAS will be operated including evasive and emergency maneuvers and maintaining appropriate distances from persons, vessels, vehicles, and structures.

·	In order to be current, the FO must have conducted and logged at least 3 launch and 3 recovery operations within the previous 90 days. These operations must have been conducted on a registered sUAS of the same class as the sUAS to be used, and in a comparable environment.

Visual Observer (VO)

The remote PIC may use a visual observer to offer a viewpoint that is distinct from the remote PIC. Depending upon the requirements of the flight operation, multiple observers may be required.

Duties and Responsibilities

·	Assist and advise the remote PIC in maintaining situational awareness and complying with duties and flight requirements.

·	Maintain a view of the flight operations and surrounding areas to scan for potentially conflicting traffic or other hazards.

·	Maintain communication with the remote PIC.

Qualifications

·	Have sufficient knowledge of the airspace in which the work detailed in this Manual will be performed to permit adequate assessment of the risks posed by other aircraft or objects

·	At a minimum, Observers will have training in the Standard Operating Guidelines and become familiar with the sUAS features, settings, and limitations.

·	Shall maintain a thorough understanding of all normal, abnormal, and emergency operational aspects of the sUAS.

·	All VO candidates must be approved by the remote PIC for TDOT sUAS flight operation.

Training and Currency

·	The VO must understand how the sUAS will be operated, including evasive and emergency maneuvers and maintaining appropriate distances from persons, vessels, vehicles, and structures.

·	The VO must be briefed by the remote PIC prior to each flight to ensure a consistent understanding of each operation.

Site Manager (SM)

A Site Manager (SM) is the person or entity in control of the site considered for the flight operation. Such entity can be the property owner, area manager, contractor superintendent, or their official delegates.

·	The remote PIC or his delegate shall coordinate with the site manager/s in control of the area planned for the flight operation to:

·	Secure permission to conduct flight operation

·	Notify all persons directly participating in the operation

·	Ensure aerial activities are coordinated to eliminate potential conflicts

·	Modify or cancel the flight operations planned or current

Operating Requirements

·	The remote PIC shall identify the flight crew and each crew member responsibility prior to the start of the flight operation.

·	The operator shall plan for the flight mission using these guidelines for assistance.

·	The operator controlling the sUAS should always avoid manned aircraft.

·	The operator shall avoid any maneuvers that can be considered careless or reckless.

·	The sUAS shall remain within the operator’s line of sight without aided sight enhancements except for conventional sight correction glasses.

·	Line of sight conditions can be supplemented by the assistance of a visual observer.

·	First Point View technology can be used by the operator or the visual observer. However, the remote PIC shall maintain the line of sight with the sUAS as required.

·	The remote PIC shall be responsible for one mission at a time. If more than one mission is conducted at the same time and location, all remote PICs shall coordinate missions prior to the start of the missions. In such case, each flight crew shall be identified and cannot be exchanged during the flight missions.

·	Flight missions shall be conducted during daylight or in twilight (30 minutes before official sunrise to 30 minutes after official sunset, local time) with appropriate anti‐ collision lighting.

·	The sUAS shall not fly over any person who is not directly participating in the operation.

·	Persons not directly participating in the flight operation shall remain under a covered structure, or inside a covered stationary vehicle.

·	Flight Operations shall be conducted from a stationary position except in sparsely populated areas. Prior approval shall be granted by TDOT prior to conducting any flight operation from mobile (non‐stationary) platforms (i.e. vehicle or boat).

·	The sUAS may be outfitted with equipment and loads within manufacturer’s approved limits and without exceeding FAA regulated 55 pounds total. The remote PIC shall approve such installation and the operator’s training prior to flight mission.

·	The sUAS may be used for load transport without conflicting with any of the other requirements.

Planning for flight Missions

The remote PIC or his delegate shall perform and document the following planning aspects prior to the flight mission.

Purpose

·	The sUAS flight missions shall be conducted to only serve the functions of The Tennessee Department of Transportation or The State of Tennessee Departments served by TDOT functions.

·	Safety is the number one goal for the operation of the sUAS. Any action, circumstance, or condition that may affect safe flight operations shall cause the remote PIC to cancel any flight mission.

·	The remote PIC shall investigate, review, and approve the sUAS and its attachments ability to achieve the intended flight goals.

·	The sUAS may be used for training and testing for flight characteristics and the function of attachments.

Location

Prior to the flight mission the remote PIC or his delegate shall plan for the flight mission using the following steps as the minimum requirements:

·	Check FAA approved sectional chart maps or maps generated using FAA sectional chart maps. The person planning for the flight must ensure the following:

o	The entire flight operation is conducted in Class G airspace.

o	If operated within 5 miles of an airport, it is recommended, but not required, that the airport operator be notified prior to the operation.

o	Operations in Class B, C, D and E airspace require an airspace authorization.

o	The flight operation area is not within any manned flight paths similar to hospital helicopter flight paths. In such case:

§	Priority shall be given to manned flights, and operators shall perform evasive maneuvers to exit and remain away from any active manned flight paths.

§	If the sUAS is occupying any airspace required for the manned flight activity, the remote PIC shall cancel the flight operation.

o	No active Temporary Flight Restrictions (TFR) is in effect for the intended flight area. Remote PIC shall check TFRs in advance and immediately prior to conducting the flight operation.

o	The following resources may be used:

§	www.tfr.faa.gov

§	B4UFly Smartphone App (Published by FAA)

§	FltPlan Go Smartphone App

§	The FAA online sectional charts (Tennessee is included in St Louis, Cincinnati, Memphis and Atlanta sectional charts): https://www.faa.gov/air_traffic/flight_info/aeronav/digital_products/vfr

§	www.FAASafety.gov has an email notification update for active TFRs

§	Online resources including:

·	https://skyvector.com/

·	http://www.iflightplanner.com/AviationCharts/

·	http://vfrmap.com/

·	The flight purpose can be achieved without exceeding the maximum allowable altitude of 400 feet above the ground level (AGL). Higher altitude can be achieved near structure if the sUAS can remain within 400 feet of a structure.

·	The location shall allow for a safe launch and recovery area without affecting any of the flight requirements.

·

·	Flight operations are performed without affecting moving traffic. Traffic control including temporary traffic closures shall be arranged in advance with the responsible TDOT office for the area.

·	The sUAS control station shall be in a safe stable location to allow for the flight crew direct attention to the flight operations without possible distraction.

Weather

Check for future weather conditions using the previously mentioned resources for guidance. The person planning for the flight must ensure the following:

·	Minimum weather visibility is three (3) miles from the control station.

·	Wind speed is within the allowed sUAS manufacturer’s limitations.

·	The maximum sUAS air speed in any direction shall not exceed 45 mph thus factoring the planned relative ground speed and direction.

·	Flight operations shall avoid weather conditions that might affect the sUAS operations unless specifically approved by the sUAS manufacturer including:

o	Rain,

o	Snow, and

o	Excessive wind

Small Unmanned Aircraft System (sUAS)

The remote PIC shall ensure:

·	The sUAS is registered with the FAA and registration number is clearly marked, secured, and visible on the sUAS.

·	Operation of sUAS shall be conducted in accordance with the manufactures checklist for the specific aircraft model.  If the manufacture does not supply a checklist, at a minimum the Remote-PIC will use the one provided in Appendix A of this SOG.

·	The airworthiness of the Small Unmanned Aircraft System in accordance with the approved manufacturer’s specification.

·	Preventive Maintenance and repair of the sUAS is current in accordance with the approved manufacturer’s specification.

·	The total weight of the sUAS including all attachments and loads does not exceed the FAA designated limit of 55 pounds.

·	The entire flight duration can be performed within allowable sUAS flight duration limits while allowing appropriate flight time for safe return and recovery for the system.

·	Staged flights shall be planned to allow for exchange of sUAS or batteries to achieve any needed extended duration.

·	Only manufacturer’s approved batteries in adequate condition with no visible signs of defects may be used for the flight operations.

·	The sUAS shall have the following features and settings

o	The flight control system shall:

§	Be equipped with low fuel or battery level indicator to allow for sufficient recovery and landing time.

§	Be equipped with a GPS unit.

§	Include a Return to Home function that can be triggered either manually by the flight operator or the remote PIC, or automatically in the case of loss of communication with the ground station.

§	Include a maximum altitude setting with the ability to set a maximum flight altitude of 400 feet.

§	Have flight stabilization features to promote safe operations by the operator.

§	Obstacle avoidance technology is a preferred feature.

§	Ability to limit the maximum ground speed in any direction to 45 mph unless such speed is unachievable by the system.

o	The Aircraft System shall:

§	Be free from any visible defects.

§	Tested for operations prior to conducting the first flight mission with three successful launch and recoveries.

§	Equipped with the appropriate attachments to enable the performance of the required planned mission in accordance with the manufacturer’s recommendations.

§	Equipped with appropriate anti‐collision lighting if the planned flight mission will be conducted during twilight time (30 minutes before official sunrise to 30 minutes after official sunset, local time).

§	Not include equipment with interfering transmission frequencies between any wireless spectrum used for:

·	Control,

·	Video/Audio streaming,

·	Aviation Telemetry,

·	GPS, or

·	Data transmission.

Before any sUAS is purchased, or used on a TDOT job site, it must first be approved by TDOT. Each vehicle must have its own operations manual to serve as an addendum to this document with vehicle‐specific operating procedures and safety protocols. All sUAS required functions as detailed above shall be in a good functioning condition as described by the sUAS manufacturer.

Appendix A

General‐Purpose UAS Checklist

A remote PIC will rely on checklists to ensure pre‐flight, in‐flight, and post‐flight checks and setup steps are always completed. sUAS Manufacturer’s Manuals will typically include checklists specific to a particular aircraft. This checklist is intended to supplement the Manufacturer’s checklist to ensure the site, personnel, and aircraft are all properly informed and prepared for each launch, flight, and recovery.

First flight of the day Checklist:

❏ Ensure the aircraft is free of visible defects.

❏ Complete aircraft assembly per Manufacturer's Manual.

❏ Ensure fasteners and parts are secure.

❏ Ensure batteries are fully charged.

❏ Check mission planning documents; ensure paperwork is complete and up‐to‐date.

Pre‐Flight Checklist:

❏ Identify the flight crew members including the operator and the visual observer/s (if any) and ensure each member has awareness of their mission, role, and responsibility.

❏ Ensure the Site Manager/s has been notified and was able to review and approve the flight operation.

❏ Establish and brief personnel on area of operation, launch/recovery zones, mission plan.

❏ Establish and brief personnel on contingency plans, failsafe point, and flight termination procedures.

❏ Ensure area is clear of non‐participating spectators and hazards.

❏ Check that wind and weather are within acceptable operational limits.

❏ Power on system and check link.

❏ Complete Manufacturer's Manual preflight checklist.

Launch Checklist:

❏ Position UAS at launch point and establish personnel at designated locations.

❏ Verify personnel are prepared; verify cleared surrounding area and airspace.

❏ Ensure all communication links are established and in a reliable working condition

❏ Initiate launch sequence per Manufacturer's Manual.

❏ Perform control maneuvers to ensure sUAS functionality and performance.

Landing Checklist:

❏ Line up sUAS for landing.

❏ Execute safe recovery sequence per Manufacturer's Manual and site‐specific approach/recovery pattern.

Shut Down / Secure Checklist:

❏ Unplug and remove UAS battery/batteries.

❏ Store batteries in a safe manner.

❏ Disassemble aircraft for transport or prepare for next flight.

❏ Complete post‐flight documentation.

Small Unmanned Aircraft System FLIGHT LOG

sUAS Registration Number:

Date:

Model:	Time:

| Flight Crew | Name |
| --- | --- |
| Remote PIC |  |
| Visual Observer |  |
| Flight Operator |  |
| Site Manager/Signature |  |
| Notified ATC Contact |  |
| Additional Role |  |
| Additional Role |  |
| Weather Conditions | Site Description |
| Cloud Conditions |  | Address/MM |  |
| Winds Speed |  | mph | City |  |
| Winds Direction |  | County |  |
| Visibility |  | nm | GPS Location |  |  |
| Precipitation |  |  | Nearby Airport Code/Distance |  | miles |
| Temperature |  | Fahrenheit |  |  | miles |
| Humidity |  |  |  |  | miles |
| NOTAMs and TFRs Checked: | YES | NO | Jobsite Airspace Classification | G E D C B |
| Flight Characteristics | System |
| Launch/Recovery time |  |  | Attachments |  |
| Launch/Recovery time |  |  |  |  |
| Launch/Recovery time |  |  | Max setup AGL | ft |
| Launch/Recovery time |  |  | Fence Distance | ft |
| Launch/Recovery time |  |  | Total Weight | lb |
| Total Flight time |  |  |  |
| Remarks |
| Delays? Reason: |  |
| Accidents? Description: |  |
| Additional: |  |
| Remote PIC Signature: |  |

Email completed Flight Logs to TDOT.UAS@tn.gov