# EXAMPLE Lead Abatement Report

A lead abatement report is to be prepared by a certified supervisor (for 10 units or less) or certified project designer (for 11 units or more).  The lead abatement report shall be submitted to the Division no less than 15-days following the completion of the abatement project.  The lead abatement report shall include the following information:

Lead Abatement Report

Lead Abatement Project Start Date:		1/1/16

Lead Abatement Project Completion Date:	1/31/16

Lead Abatement Project Address:			111 Main Street

Nashville, TN  30000

Date of Building (House) Construction:		1968

Owner Name:					John Doe

Owner Address:					111 Main Street

Nashville, TN  37000

(615) 555-5555

Certified Supervisor Information:			James Doe,

Certification # TNLBP 2002-03S

Certified Abatement Firm Information:		James Doe Environmental, Inc.

Certification # FTN 2002

Certified Abatement Firm Address:		401 Church Street

Nashville, TN  37000

Phone:  (615) 555-5551

Inspection / Risk Assessment Conducted by:	Linda Doe,

Certification # TNLBP 2002-02IRA

333 Main Street

Nashville, TN 37000

Phone:  (615) 555-5552

Date Inspection / Risk Assessment conducted:	April 2, 2001

Clearance Testing Conducted by:			Linda Doe,

Certification # TNLBP 2002-02IRA

333 Main Street

Nashville, TN 37000

Phone:  (615) 555-5552

Date Clearance Testing Conducted:	 	January 31, 2001

Name and Address of the recognized

National Lead Laboratory (NLLP) that

analyzed the samples: 				LYZ Laboratory

Contact Person: Mr. Labin

321 Far Street

Nashville, TN  37000

Phone: (615) 555-2222

## I.	Pre-Abatement Information

Job Specifications:

A detailed written description of the abatement, including abatement methods used, location of rooms and/or components where abatement occurred, reason for selecting particular abatement methods for each component, and any suggested monitoring of encapsulants or enclosures.

(Note: A table format may be used to comply this information.)

1.	All windows were replaced and sealed with lifetime caulking.

2.	All interior kitchen trim was encapsulated except casing /header over ‘C” door which was replaced.

3.	All interior surfaces were cleaned using the HUD cleaning method: HEPA, TSP wash, rinse, HEPA.

4.	Exterior doors and ‘A’ and ‘C’ sides were replaced.

5.	Exterior exposed painted surfaces were covered with tyvek (housewrap) and enclosed with aluminum/vinyl or replace.  These surfaces included but were not limited to:

-Vinyl siding installed over fan fold;

-Vinyl soffit covering the soffit and porch ceilings;

- Back-caulked aluminum flashing around windows, doors, fascia;

- Porch posts and lattice were replaced.

6.	Perimeter lead-contaminated soil was removed in play area ‘C’.  The area was cover with soil that is not lead-contaminated.  The area was seeded and covered with straw.

Operation and Maintenance Plan

1.	Enclosures should be monitored on a yearly basis to ensure continued efficiency.

- Interior encapsulated trim should be monitored one month, six months and annually thereafter, and redone as necessary.

(Note:  If areas of frequent damage occur, these areas should be protected with a enclosure system.)

(Note:	Typically, sections of your abatement plan should be included here.  Information should be altered to only include work completed.)

Occupant Protection

A written occupant protection plan developed specifically for the abatement project            pursuant to Rule 1200-1-18.01(8)e(5).

(Note:  Add the Occupant Protection Plan in the document or list it as an attachment.)

Copy of Inspection and/or Risk Assessor Report signed by a State of Tennessee certified lead-based paint inspector/risk assessor and prepared pursuant to Rule 1200-1-18.01(8)b(4); c(5); and/or d(11) with the inspection results expressed in terms appropriate for the sampling method(s) for all media tested (such as exterior and interior components, soil, etc.)

- Post-Abatement Information

Post-abatement clearance procedures conducted pursuant to Rule 1200-1-18-.01(8)e(9) and (10).

Copy of clearance testing results and all soil analyses (if applicable) indicating whether the unit passed, or failed.  If failed the measures used to reach clearance must be documented and the second clearance testing results must be included.

Hazardous Waste Disposal

All potential hazardous waste from paint chips, HEPA vacuum, peel-away, etc. collection are accumulated off-site.  If less than 220 lbs. is accumulated per month it may be possible to dispose of the waste as nonhazardous waste from a small quantity generator after checking with the state and solid waste facility.  Dispose of the waste through a certified hazardous waste hauler according to state and local laws. (EPA Model Lead-Based Paint Abatement Worker Training Course - Ch. 8)

Pursuant to Chapter Rule 1200-1-18-06 Residential Property Renovation requires each person who performs a renovation of target housing for compensation to provide a lead hazard information pamphlet, Protect Your Family From Lead In Your Home, to the owner and occupant of such housing prior to commencing the renovation.

This Lead Abatement Report was completed by:

James Doe,

Certification # TNLBP 2002-03S

Date:	____/ _____/ _______

___________________________________________Signature